## Slide 1: GridMind
ET AI HACKATHON: AGENTIC EDITION · PROBLEM 4, UTILITIES
An agentic orchestrator for a solar, wind and battery portfolio, re-planned every 15 minutes
[Team name] · [Team members]
Case client: Deccan Renewables Pvt. Ltd., Karnataka (fictional)
Self-assessed position: D2 / F3
Notes: Open with the one-line pitch: GridMind runs a renewable portfolio on a 15-minute loop. An LLM-driven agent chooses the strategy, a solver computes the megawatts, and code checks safety before anything executes. We claim D2 / F3 and the deck shows why.

## Slide 2: A portfolio that changes every 15 minutes
THE CASE
740 MW
Generation: 5 solar parks and 3 wind farms across Karnataka
400 MWh
Storage: 2 batteries, 100 MW combined, 4-hour duration
300 MW
Contracted load: steel, data centre, textile and cement customers
150 / 200
Grid limits in MW: import from and export to the market
What changes mid-shift
Clouds cut solar output
Wind surges or drops
Market prices spike
A battery trips offline
A transmission line derates
Industrial demand jumps
Forecasts are revised
A storm alert arrives
Notes: This is the scenario from the problem statement, made concrete: a fictional Karnataka utility, Deccan Renewables. The user is the shift dispatch manager at the control room desk. Every one of the eight disturbances shown is something the demo can inject.

## Slide 3: Four levers, and goals that pull against each other
THE DECISION
Batteries
Charge, discharge, or hold a reserve for an emergency
Market
Buy from the grid, sell to it, or wait for a better price
Renewables
Use all of it, or curtail solar and wind when it cannot be moved
Demand
Call paid demand response; never shed a customer's critical load
Minimise
Electricity cost, carbon emissions, renewable curtailment, battery wear
Maximise
Reliability of contracted supply, renewable utilisation, margin
What a wrong call costs
₹15,000 per MWh of contract shortfall. ₹1,00,000 per MWh of lost critical load.
Penalty rates are case assumptions set in config.
Notes: The problem statement stresses that this is not classical single-objective optimisation. The operator has four groups of actions and at least six goals that conflict. The penalties on the right are the assumptions we configured for the case; they are what make a wrong call expensive.

## Slide 4: The agent decides how to run the portfolio. A solver decides the megawatts. Code decides whether it is safe to execute.
THE DESIGN PRINCIPLE
The language model never produces a dispatch number. It chooses an operating mode, sets the trade-off weights, compares candidate plans and explains the result to the operator.
Notes: This is the idea the whole architecture hangs on. It is how we get agentic behaviour and demonstrable reliability at once: reasoning is the model's job, arithmetic is the solver's job, and safety is plain code.

## Slide 5: One closed loop, run every 15 minutes
ARCHITECTURE · PROCESS FLOW
STEP 1
Sense
Simulator
Steps every asset by 15 minutes
Forecaster
P10, P50, P90 for the next 8 hours
Event engine
Injects clouds, outages, price spikes
STEP 2
Reason
Monitor agent
Flags anomalies, triggers a re-plan
Strategy agent
Picks a mode and weights, calls tools
Tools
Solver, risk evaluator, plan comparison
STEP 3
Gate
Guardrails
Hard checks on every candidate plan
Recovery
Two re-solves, then safe-mode dispatch
Operator
Approves, pauses or overrides
STEP 4
Act and record
Executor
Applies only the first 15-minute step
Decision log
One audit entry per interval
Explainer agent
Writes the operator's shift briefing
The executed step changes the simulated grid state, fresh telemetry arrives, and the loop starts again at step 1.
Notes: Walk left to right. Sense: the simulator and forecaster give the current state and an 8-hour view with uncertainty bands. Reason: the monitor decides whether anything needs a re-plan, the strategy agent picks an operating mode and calls its three tools. Gate: every candidate plan passes deterministic guardrails; if it fails twice, a safe-mode heuristic takes over. Act: only the first interval is executed, everything is logged, and the explainer writes the briefing shown on the dashboard. The full component table is in ARCHITECTURE.md.

## Slide 6: Where the model is used, and where it is not
ARCHITECTURE · MODEL USAGE
Component | Job | Built as
Monitor agent | Turns telemetry deviations into a short situation summary | LLM + code
Strategy agent | Chooses the operating mode and weights, compares plans | LLM + code
Explainer agent | Writes what was done, why, and what would change it | LLM + code
MILP optimiser | Computes every MW setpoint over a 32-interval horizon | Deterministic
Risk evaluator | Scores each plan against 20 Monte Carlo scenarios | Deterministic
Guardrails | Reject any plan that breaks a hard physical or contract limit | Deterministic
Executor and log | Apply the approved step and record the full decision | Deterministic
Model: Gemini 2.5 Flash, at most 6 tool calls per cycle, every output validated against a Pydantic schema. If a call fails or returns an invalid shape, a rule-based stand-in returns the same schema, so the loop never stops.
Notes: The brief asks for model usage to be explicit. Three components use the LLM, and all three are about judgement and language. The four shaded rows are deterministic. The rule-based stand-in is also how the system runs fully offline. Solver: PuLP with CBC.

## Slide 7: Optimality criteria: six modes, one hierarchy
ARCHITECTURE · KEY DECISIONS
Mode | Cost | Carbon | Curtail | Wear | Reliab. | Reserve
Green | 1.0 | 2.5 | 3.0 | 0.8 | 3.0 | 15%
Economic | 3.5 | 0.8 | 1.0 | 1.2 | 2.5 | 10%
Reliability first | 1.0 | 0.5 | 0.5 | 0.5 | 5.0 | 35%
Storm preparation | 0.5 | 0.5 | 0.5 | 0.5 | 5.0 | 60%
Outage recovery | 1.2 | 1.0 | 1.0 | 0.5 | 4.5 | 35%
Congestion management | 2.0 | 1.0 | 3.0 | 0.8 | 3.5 | 20%
The strategy agent picks the mode from the situation. Each mode is a set of objective weights (0 to 5) plus a battery reserve floor; the solver minimises the weighted sum inside hard physical constraints.
When goals conflict
₹1,00,000 / MWh
Lost critical load
₹25,000 / MWh
Breaching the reserve floor
₹15,000 / MWh
Contract shortfall
₹10,000 / MWh
Highest market price
Notes: The brief says the solution should make the optimality criteria clear and show how actions are chosen when objectives conflict. The table answers the first half: six named modes, each a weight vector and a reserve floor. The ladder answers the second half: penalties are ordered so that protecting critical load always beats holding reserve, which beats avoiding a contract shortfall, which beats any market price. Battery wear is priced at ₹500 per MWh of throughput, so the batteries only cycle when the price spread justifies it.

## Slide 8: Plan for a range, commit to 15 minutes
ARCHITECTURE · UNCERTAINTY
P10 · P50 · P90
Forecast as a cone
Every interval, each asset gets a pessimistic, expected and optimistic forecast for the next 32 intervals (8 hours).
20 scenarios
Test each candidate plan
Monte Carlo runs give expected cost, P90 tail cost and the probability of a contract shortfall, so plans are compared on risk.
1 of 32 steps
Execute only the first
The solver plans 8 hours but only the first 15 minutes run. The plan is rebuilt next interval, so forecast errors do not pile up.
Nine disturbance types the simulator can inject
Cloud cover
Wind surge
Wind drop
Battery outage
Price spike
Storm alert
Line constraint
Demand surge
Forecast update
Notes: Three layers of uncertainty handling. Forecast cones instead of point forecasts. Monte Carlo scoring of each candidate plan so the agent compares tail risk, not just expected cost. And rolling re-planning: only the first interval of each 8-hour plan is ever executed. The nine disturbance types cover every example in the problem statement. This slide is the basis of the F2 and F3 claims.

## Slide 9: Nothing executes until code approves it
ARCHITECTURE · SAFETY AND FAULT TOLERANCE
Checked before every dispatch
The solver returned an optimal plan
Battery charge stays inside its 10% to 95% band
No battery charges and discharges at once
No command goes to an unavailable battery
Battery and grid power stay within rated limits
No buying and selling in the same interval
No critical customer load is shed
Demand response stays within contract maximums
Generation and load balance
If something fails
The model call fails or times out
A rule-based stand-in returns the same schema
The model output fails validation
One repair attempt, then the stand-in
Guardrails reject the plan
Re-solve with more weight on reliability, up to twice
Still rejected: safe mode
Hold 40% battery reserve, export nothing, serve critical load
The operator can pause, step, approve or override at any interval.
Notes: This slide is the reliability argument behind D2. On the left, the hard checks every plan passes before it reaches the executor. On the right, the fallback ladder: the system degrades in steps and always ends in a known-safe dispatch. Human oversight sits on top: the operator can pause, step through intervals, require approval, or override a setpoint, and overrides are logged.

## Slide 10: A day at Deccan Renewables: five disturbances
WORKING DEMO
Time | Event | What is injected
10:30 | Cloud cover | Two solar parks lose 60% of output for 2 hours, with no warning
12:00 | Storm alert | Announced 6 hours before an 18:00 arrival: solar down 80%, export capped at 80 MW
14:00 | Battery outage | Battery B2 (40 MW) is unavailable for 4 hours, with no warning
16:00 | Line constraint | Export corridor limited to 120 MW for 2 hours, with 1 hour of notice
19:00 | Price spike | Market price doubles for 1 hour, with 30 minutes of notice
Runs locally with one command: ./scripts/run_demo.sh
Eight dashboard pages
Control Room
Event Injector
Agent Reasoning
Decision Log
Scenario Comparison
Reliability Report
Data and Assumptions
Architecture
Any event can also be injected live, so judges can pick the disturbance.
Notes: Switch to the live dashboard here. Run the preset day in the Control Room, pause after each event, and open Agent Reasoning to show the mode chosen, the tool calls made and the plans compared. Then open the Decision Log to show the audit entry for that interval. Offer to inject an event of the judges' choosing from the Event Injector.

## Slide 11: One simulated day, three strategies
EVIDENCE · BENCHMARK
44.5% lower
Net operating cost against the rule baseline
88.7% lower
Contract shortfall, in MWh not delivered
0 MWh
Critical load shed; the baseline shed 43.2 MWh
Metric over 24 hours | Rule baseline | Fixed-weight solver | GridMind agent
Net cost (₹ crore) | 4.09 | 2.28 | 2.27
Contract shortfall (MWh) | 1,312 | 154 | 148
Critical load unserved (MWh) | 43.2 | 0.0 | 0.0
Carbon emissions (tCO2) | 1,875 | 1,803 | 1,769
Hard safety violations | 0 | 0 | 0
Most of the saving comes from optimising instead of following rules. The agent's mode switching adds a further ₹84,000 on this day and gives the lowest shortfall and carbon of the three. Summer day with injected disturbances; same conditions for all three.
Notes: All three strategies face the same summer weather and the same injected disturbances. The rule baseline is a conventional if-then dispatch. The fixed-weight solver is the same optimiser with one static objective. GridMind adds the agent layer that changes mode and weights as the day unfolds. Be direct about the breakdown: the large gap is rules versus optimisation; the agent's incremental gain on cost is small on this day. Presenter check before the session: confirm whether these figures were produced with the live model or the rule-based stand-in, and say which.

## Slide 12: 30 simulated days, zero hard violations
EVIDENCE · RELIABILITY
2,880
Consecutive 15-minute intervals
21
Disturbances injected at random
57
Automated tests, all passing
0
Hard-constraint violations
0 MWh
Critical customer load unserved
0
Intervals that fell back to safe mode
Across the run: mean daily net cost ₹1.44 crore (P90 ₹2.20 crore), mean contract shortfall 82.9 MWh a day, mean curtailment 0.16 MWh a day. Summer and monsoon days alternate.
Reproduce with: python scripts/run_reliability.py
Notes: This is the evidence for 'high degree of demonstrable reliability'. Thirty days back to back, 21 random disturbances, and not one hard-constraint violation or megawatt-hour of critical load lost. Note what is and is not zero: contract shortfall is not zero, because shortfall is a priced trade-off, not a hard constraint. The run takes about six minutes and anyone can reproduce it.

## Slide 13: We claim D2 / F3
OUR POSITION ON THE 3×3 GRID
F1
F2
F3
D1
D2
GridMind
D3
D = solution depth, F = solution features, as defined in the brief.
Depth D2: structured input, high demonstrable reliability
Inputs are structured telemetry, forecasts and event notices. Zero hard violations in 2,880 intervals, guardrails before every action, an audit entry for every decision.
Features F3: simulate over time as inputs vary
F1: the solver picks one joint action set across batteries, market, curtailment and demand response
F2: the agent sets mode and weights for the situation, then compares plans on Monte Carlo risk
F3: rolling 8-hour horizon, a 30-day run, two seasons, nine disturbance types
Not claimed: D3
No multimodal input such as satellite imagery or camera feeds.
Notes: The brief penalises both over- and under-estimation, so state the claim and the reasoning plainly. D2 because inputs are structured and reliability is demonstrated, not asserted. F3 because the system does everything F1 and F2 require and also simulates the portfolio over time under varying inputs. We stop short of D3 because nothing in the system reads images, audio or other unstructured sensor data.

## Slide 14: Eight criteria, and where to look for each
AGAINST THE EVALUATION FRAMEWORK
Significance
Dispatch every 15 minutes is a real control-room job with priced penalties
Innovation
An LLM steers a solver's objective instead of producing numbers itself
Effective use of AI
The model handles judgement and language; maths stays with the solver
Technical execution
MILP, Monte Carlo risk, forecast cones, guardrails, 57 passing tests
Agentic capability
Monitors, plans, calls tools, recovers from rejected plans, then acts
Business impact
44.5% lower cost and 88.7% less shortfall on the benchmark day
Prototype quality
Eight-page dashboard, live event injection, one-command local run
Scale and responsible AI
Config-driven assets, operator approval and override, full audit log
Notes: A map for the judges: the eight evaluation parameters from the brief, each with the one piece of evidence that answers it. Use this slide to take questions; each card points back to an earlier slide or a dashboard page.

## Slide 15: What the prototype does not do yet
SCOPE
Outside the current build
Grid frequency is not modelled or controlled
Maintenance scheduling and crew dispatch are not agent actions
Inputs are structured only: no imagery or video
It runs on a simulator. Weather is historical Open-Meteo data; prices and demand are modelled series
What comes next
Live plant telemetry and market price feeds in place of the simulator
Maintenance windows as a decision the agent can move
Larger portfolios: the solver's problem size grows linearly with the number of assets
Notes: Say this before the judges ask. The brief lists grid frequency and maintenance actions among possible inputs and actions; we chose not to cover them, and we do not claim them. Everything shown runs on a simulator built from real historical weather for the eight sites and modelled price and demand series.

## Slide 16: The agent sets the strategy, the solver sets the megawatts, and code keeps every dispatch safe
GRIDMIND IN ONE LINE
Working demo
Eight-page control room, run locally with ./scripts/run_demo.sh
Architecture and code
github.com/varunbhaskar31/gridmind, with ARCHITECTURE.md
Position claimed
D2 / F3, backed by a 30-day run with zero hard violations
Notes: Close on the two things the brief asks every submission to include, a working demo and a detailed structural architecture, and restate the claim. Then take questions; the evaluation slide is the best one to return to.